Practical Work :Conversion of sampling rate and STFT

I- Conversion of sampling rate

 2

 H
   3
1.

We can only up/down-sample by an integer factor (we can’t downscale by factor 2/3) and in order to limit the frenquencies as less as possible, we do the up-sampling by factor 2 first, then the down-sampling by factor 3 next. For the filter H we take : H( e^{2i%pi%nu} )=2 * 1_{ [-%nu_c,%nu_c] }( %nu ) where %nu_c=min( 1 over{2*2},1 over{2*3} )=1 over 6 drarrow H( e^{2i%pi%nu} )=2 * 1_{ [-{1 over 6},{1 over 6}] }( %nu )

4.
 2

   3

 z-1

W
X
Z
Y

X(z) = W(z²), Y(z)=z-1X(z), Z(z)= 1 over 3 sum from{k=0} to{2} Y( z^{1over3}e^{{2ik%pi}over3} )=1 over 3 sum from{k=0} to{2} z^{-1over3}e^{{-2ik%pi}over3}W( z^{2over3}e^{{4ik%pi}over3} )

X
Y
Z
W
V

 2

   3

 z-1
 z

W(z) = zV(z), X(z)= 1 over 3 sum from{k=0} to{2} W( z^{1over3}e^{{2ik%pi}over3} ) , Y(z) = X(z²), Z(z)=z-1Y(z)

so Z(z) = z-1X(z²) = z^{-1}1 over 3 sum from{k=0} to{2} W( z^{2over3}e^{{4ik%pi}over3} )=z^{-1}1 over 3 sum from{k=0} to{2} z^{2over3}e^{{4ik%pi}over3}V( z^{2over3}e^{{4ik%pi}over3} ) , e^{{4ik%pi}over3}*e^{{-6ik%pi}over3}=e^{{-2ik%pi}over3} and e^{{-6ik%pi}over3} =1

Those two diagrams are equivalent.